## Slide 1: Transmission Control Protocol
Presented By:
Sabin Nepal
Rajan Bhattarai
Achut Dahal
Aruna Shrestha

## Slide 2: Table of content
Introduction to TCP
Features of TCP
TCP header
Connection management
Flow control
Error control

## Slide 3: Introduction to TCP
A reliable, connection-oriented transport protocol
protocol for data transmission in communication network such as internet
provides a reliable stream delivery and connection service to applications
corresponds to the transport layer of TCP/IP suite
Used in World Wide Web (WWW),E-mail, File Transfer Protocol, Secure Shell, peer-to-peer file sharing, and some streaming media applications.

## Slide 4: Features
Numbering system
Sequence number
Acknowledgement number
Error control
Flow control

## Slide 5: Services
Process to process communication
Stream delivery service
Full duplex-communication
Connection-oriented service
Reliable service

## Slide 6: TCP header

## Slide 7: TCP connection
Establishes a virtual path between source and destination
works in Server/Client model
TCP uses the services of IP to deliver individual segments, but it controls the connection itself
Transmission requires 3 phases
  Connection established
  Data transfer
  Connection termination

## Slide 8: Connection Establishment
SYN:
  Synchronization of sequence no’s
  Consumes 1 sequence no
  Carries no real data
SYN+ACK
  SYN segment for communication in other
  direction and ACK for the received SYN,
  Consumes 1 sequence no
  ACK
  Just an ACK segment
  Does not consume any sequence number

## Slide 9: Data Transfer
Pushing data
  Increase efficiency of data
  Sending and receiving buffers the data
  Delivers to application program on ready
Urgent data
  Application program send urgent bytes
  Sending application program want a piece
  Of program to read out which is handled by
  URG bit

## Slide 10: Connection termination
FIN
  Consumes 1 sequence no
  May or may not consume data
FIN+ACK
  Consumes 1 sequence no
  FIN announce closing of connection In other
  Direction and ACK for received FIN
ACK
  Does not consume any sequence no

## Slide 11: Flow Control
TCP uses sliding window to handle flow control
Technique to properly match the transmission rate of the sender to that of the receiver and network

## Slide 12: Error Control
Error detection and correction is achieved of three simple tools
  Checksum
    Includes 16-bit checksum in every segment which is used to check for corrupt segment
    If corrupted, it is discarded by destination TCP and is considered lost
  Acknowledgement
    TCP uses acknowledgement to confirm the receipt of data segments

## Slide 13
  ACK segments are never acknowledged
Retransmission
  Lost, delayed or corrupted data are retransmitted
  Segment is retransmitted either when a retransmission timer expires or when sender receives three duplicate ACK’s
    Retransmission after RTO
    Retransmission after 3 duplicate ACK’s
    Out of order segments

## Slide 14: References
https://www.tutorialspoint.com/data_communication_computer_network/transmission_control_protocol.htm
https://www.slideshare.net/k33a/transmission-control-protocol-tcp-31902778
https://www.slideshare.net/k33a/transmission-control-protocol-tcp-31902778